## Slide 1: 28-GHz Class-F-1 Power Amplifier with Coupled-Inductor based Harmonic Impedance Modulator
Seyed Yahya Mortazavi
Kwang-Jin Koh
Multifunctional Integrated Circuits & Systems Group
Virginia Tech, Blacksburg, VA

## Slide 2
Background / Motivation
- PA Requirements for 5G Applications
- Challenge in Silicon mm-Wave PAs
- Efficiency of mm-Wave PAs
- Harmonic Tuned (Class-F-1, Class-F) PAs
Coupled Inductor Based Class-F-1 PA Design
Measurement Results
Conclusion
Outline

## Slide 3: Silicon PA Arrays for 5G
28 GHz band can be used for small cells (<200m) in future 5G cellular networks (worst case path-loss of <1.6dB).
Challenges of 28GHz band due to narrow beam :
  High directivity.
  Sensitivity to blockage.
  Sensitivity to mobility of the users.
Steerable beams, and Beamforming techniques: PA arrays.

Notes: 28GHz bands are suitable for 5G small cells because of availability of spectrum and acceptable path loss.
However, Directivity, sensitivity to blockage and mobility of the user are main challenges of mm-wave communication
Employing steerable beams with PA/antenna arrays enables cellular communication at 28 bands.
There are critical issues need to be resolved in mm-wave communication

## Slide 4: Efficiency & Output Power in Si PAs
Challenges of Silicon PAs:
Low break-down voltage.
Break-down / speed trade-off: limits achievable power added efficiency.
Harmonic tuned approach is promising for improving PAE of unit PA:
  So far reported highest PAE (e.g. 40% in Class F-1) at 28GHz with Pout ~ 17dBm.
Silicon PAs
- It is critical to improve unit PA’s PAE to improve overall PAE in a PA-array.
~70-90% Combining Loss
Class F-1
Class E
Notes: This figure shows the PAE-Pout of state-of-the-art silicon PAs. With Pout and PAE of current designs, regarding array or combining loss we can get ~30% PAE for the required ~25-30dBm output power.
To improve array efficiency it is critical to improve unit PA efficiency which is challenging due to low break down and speed of the silicon devices.

## Slide 5
Class-F-1 V-I Waveforms and Performance
Vknee also degrades efficiency: h ~90%x(VCC-Vknee)/VCC = 72% if VCC=2.5V & Vknee=0.5V.
non-overlap V-I: h ~100%
infinite # of harmonics control
2nd-3rd harmonics control
Overlapped V-I: h ~90%

## Slide 6
Freq. (GHz)
|ZLoad| (W)
Mode Transition from Class F-1 to Class F.
PAE > 36.5% over 25% fractional BW (24-31GHz).
Psat ~ 50mW.
[SY. Mortazavi, et al. ISSCC 2014]
Harmonic Tuning for Efficiency (Previous works)
Notes: In previous work, by tuning 2nd/3rd harmonics and mode transition from F-1 to F >36.5% PAE achieved over 25% fractional BW.

## Slide 7
Multi-resonance LC Parallel Network
Series Network
Freq. (GHz)
|ZPL|
|ZSL|
|ZTL|
|ZLoad| (W)
Peak PAE : 38.5% @ 38GHz.
Psat ~ 50mW.
Small Signal Gain: 16.5dB.
Peak PAE bandwidth ~ 6%
[SY. Mortazavi, et al. RFIC 2015]
Harmonic Tuning for Efficiency (Previous works)
Notes: In an other work, by using multi-resonance LC network, Peak PAE of 38.5% @ 38GHz achieved in Class F-1 by making O.C at 2nd harmonic and S.C at 3rd harmonic.

## Slide 8
Coupled inductor (L1-L2) impedance variation over harmonic frequencies plays a key role in harmonic modulation for Class-F-1 Load.
Impedance seen from base is < 300-Ω, Limiting VCE, peak (~ 5V) by BVCBO (~5.5V).
Proposed Coupled-Inductor Based Tuning Class F-1
Notes: In this work, we used coupled inductors to modulate 2nd 3rd harmonic load for F-1 PA. this load provides wide BW high impedance at 2nd harmonic and increases PAE-BW.
Also, Q enhancement helps to achieve higher PAE.
I will talk about details of this design in next few slides.

## Slide 9: Inductor-Based Harmonic Modulation(1)
Effective inductance of primary and secondary changes depending on magnitude (A) and phase (f ) and of current ratio (i2/i1):
  f = -p/2 : Leff1 = L1 & Leff2 = L2.
  f = 0 : Leff1 > L1 & Leff2 > L2, Q-Enhancement.
  f = p : Leff1 < L1 & Leff2 < L2, could be capacitive (negative inductance).
Notes: … which is used for load modulation in this work

## Slide 10: Inductor-Based Harmonic Modulation(2)
Resistance appears at both primary and secondary depending on magnitude (A) and phase (f ) and of current ratio (i2/i1):
  f = -p/2 : Reff1 >0 & Reff2 <0, takes signal from primary to secondary.
  f = 0 : Reff1 =0 & Reff2 =0.
  f = p : Reff1 =0 & Reff2 =0.
Notes: Also, in coupled inductors, when induced current is in-phase or out-of-phase with voltage, positive or negative resistance appears at primary or secondary.

## Slide 11
ZP & ZS comprise multi-resonance harmonic tuned load, cooperatively shaping an optimum load impedance for Class-F-1.
C3 includes collector-node parasitic capacitances including layout parasitics.
Coupled-Inductor Based Harmonic Tuning
Notes: Transistor load network is Parallel connection of the series path to the output load and parallel path which includes parasitic Caps at collector node.

## Slide 12
Load Network Operation @ f0-band (1)
The parallel inductive path resonates C3 and provides high impedance.
ZP = High Z (>10Ropt)
ZS = Ropt
Leff1-C1 is below resonance frequency: i1 & iopt are in-phase
f = -p/2
Notes: Start with series path: at f0-band

## Slide 13
Load Network Operation @ f0-band (2)
f = -p/2:
  The signal loss by Reff1 at primary is fed back to the signal path by negative resistance Reff2 at secondary.

## Slide 14
Load Network Operation @ 2f0-band (1)
In the series path the Leff1-C1 resonator provides High-Z.
The parallel inductive path resonated C3 and provides high impedance.
ZP = High Z (>2Ropt)
ZS = High Z (>2Ropt)
f = 0

## Slide 15
Load Network Operation @ 2f0-band (2)
As frequency increases, A = |i2/i1| decreases: Leff1 decreases with frequency and resonates C1 over all 2f0-band.
Notes: ------ the network is designed to resonate

## Slide 16
Load Network Operation @ 3f0-band (1)
Both paths make series resonation and short the collector to gnd.
ZP = Low Z (<1/3Ropt)
ZS = Low Z (<1/3Ropt)

## Slide 17
Load Network Operation @ 3f0-band (2)
f = p:
  Primary is inductive and secondary is capacitive.
Series resonation in both paths at 3f0-band provides low impedance (<1/3Ropt).

## Slide 18
Load Network For Class F-1 PA
f0-band
2f0-band
3f0-band
Load network provides:
  Ropt @ f0-band.
  >5Ropt : High-Z @ 2f0-band.
  <1/3Ropt : Low-Z @ 3f0-band.
Output PA operates in Class F-1 mode.
Notes: In summary,

## Slide 19: Class AB Driving and Inter-stage Matching
Optimal matching for both high Pinter-stage (>9dBm) and driving stage PAE (>35%).
Notes: And pi-matching interstate network matches small impedance seen from base of Q2 to optimal impedance
Of overlapped region of peak PAE>34% and Pinter-stage>8 contours ( from load pull simulations)

## Slide 20: Chip Photograph
IBM 8HP 0.13 mm SiGe BiCMOS (fT=180GHz, fmax=200GHz)
Chip area: 0.55x0.96 mm2 (w/i pads)
0.96 mm
0.55 mm

## Slide 21: Small-Signal S-Parameters
SOLT calibration
Class-AB biasing VCC2/VCC2= 2/2.4V
ICC1/ICC2=3/10mA
GSG
GSG
GPPG
S21 = 18-21.5dB : 27~31GHz
S11 < -10dB : 27~31GHz
S22 < -10dB : 27.5~28.5GHz
K-factor > 1

## Slide 22: Large-Signal Performance (1)
Measurement @ 28GHz
R&S Spectrum Analyzer (FSU43)
R&S Power Sensors
(Z57)
R&S Signal Source (SMA40)
Peak PAE: 42.1% @ 15dBm output power.
OP-1dB: 14.5dBm.
Psat: 16.6dBm.
Class-AB biasing: VCC2/VCC2= 2/2.4V, ICC1/ICC2=3/10mA.
Notes: Cable loss

## Slide 23: Large-Signal Performance (2)
Peak PAE >41% : 28~29GHz.
Peak PAE >37% : 27~31GHz.
Peak PAE >38% : VCC2 = 1.7-2.5V.
4 dB Pout variation for 1 V supply variation: 1.5 < VCC2 < 2.5.
@ VCC2 = 2.4V
@ fRF = 28GHz

## Slide 24: Linearity Measurement Set-up
R&S Spectrum Analyzer (FSW67)
R&S Modulated Signal Source (SMW200A)
Test Signal:
  BW=8.4MHz @ 28GHz.
  Raised cosine filtering (roll-off factor: 0.2).
  QPSK/8PSK/16QAM/64QAM/128QAM.
Notes: Here is the set-up for linearity measurements.

## Slide 25: In-band Linearity Measurements
Pout,ave / PE for ≤5% EVM is:
  13.5dBm / 32% for QPSK/8PSK.
  10.5dBm / 21% for 16QAM and 128QAM (PAPR: ~3dB).
  10dBm / 21% for 64QAM (PAPR: ~3dB).

## Slide 26: Out-of-band Linearity Measurements
ACPR > 33dB for all modulations at 6-dB back-off.
ACPR > 23dB for all modulations at output P-1dB.

## Slide 27: PAE Performance Comparison
Class F-1 with 2nd-3rd harmonic tuning proves promising for mm-Wave high efficiency PAs.

## Slide 28: Conclusion
Coupled-inductor based 2nd & 3rd harmonic tuning load proposed for mm-Wave Class F-1 PA.
2-stage Class F-1 silicon PA at 28GHz successfully implemented achieving one of the highest PAEs, 42.1%.
The proposed high efficiency PA with OP-1dB = 14.5dBm and 21.5dB gain can be used in beamforming PA arrays for future 5G applications.

## Slide 29: Acknowledgement
The authors would like to thank Lockheed Martin for the silicon chip fabrication and Rohde & Schwartz for their help in the measurement equipment.